## Slide 1
Network Security: SSH, Port Security, Hardening

## Slide 2
PC 0
PC 1
01
02
192.168.1.5
192.168.1.6
192.168.1.100

## Slide 3: Lab 1: Device Hardening (System Security)
enable
configure terminal
hostname Iraq-Switch
enable secret 12345
service password-encryption
banner motd # Unauthorized Access Strictly Prohibited #
line console 0
password ConsolePass
login
exit

## Slide 4: Lab 2: Management Security (SSH Configuration)
interface vlan 1
ip address 192.168.1.10 255.255.255.0
no shutdown
exit
ip domain-name academy.local
crypto key generate rsa
# Type 1024 when prompted
username admin secret admin123
line vty 0 4
transport input ssh
login local
exit
ssh -l admin 192.168.1.10

## Slide 5: Lab 3: Port Security (Layer 2 Security)
enable
configure terminal
interface vlan 1
ip address 192.168.1.10 255.255.255.0
no shutdown
exit
interface fa0/1
switchport mode access
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation shutdown
exit
do write

## Slide 6: Lab 4: Verification & Maintenance (Commands)
# To save all configurations:
do write
# To check Port Security status:
show port-security interface fa0/1
# To check SSH status:
show ip ssh
# To reset a port after a violation (Err-disabled):
interface fa0/1
shutdown
no shutdown
exit

## Slide 7: Shutdown All Ports
interface range fa0/1 - 24
shutdown
Port Security Range
interface range fa0/1 - 10
switchport mode access
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation shutdown
Re-enable Ports
interface range fa0/1 - 24
no shutdown